## Slide 1
Real-Time AI-Assisted Microscopic Tumor Margin Assessment in Breast Histopathology Using YOLO-Seg
A Proof of Concept on H&E-Stained Slides
Hala Hamza Rawashdeh · Razan Mohammad Essam Al-Jabban
Faculty of AI Engineering, Syrian Private University · Graduation Project 2026–2027

## Slide 2
Introduction
2
Breast-conserving surgery aims to remove the whole tumor while sparing healthy tissue
Margin status (distance from tumor to the tissue edge) is normally confirmed by pathology, days after surgery
Positive or close margins can mean a second operation
Idea: use a deep-learning segmentation model on microscope images to measure the margin in millimetres, live
Scope: proof of concept for decision support, not a medical device. The final decision stays with the surgeon and pathologist

## Slide 3
Problem Statement
3
Clinical need
Margin results arrive late
Re-excision surgery when margins are inadequate
Technical challenge
Tumor must be segmented, then measured in mm
Domain shift: public data vs. university microscope images
Evaluation issue
High Dice does not guarantee a correct margin call
Need distance error in mm and per-frame latency

## Slide 4
Literature Review
4
Ultrasound
Real-time YOLO11 biopsy navigation (Shao 2025)
Lumpectomy margin prediction (Veluponnar 2023)
Metrics vs. clinical success (Yeung 2024)
Specimen imaging
Micro-PET-CT segmentation (Maris 2025)
Specimen mammography margin width (arXiv 2024)
SAM-refined margin masks (Ward 2025)
Data & methods
BCSS histology dataset (Amgad 2019)
YOLOv8 for breast lesions (Alhsnony 2024)
YOLOv8 vs. YOLOv12 in surgery (Zheng 2026)

## Slide 5
Key Research Papers
5
Paper | What it does | What we take from it
Shao et al., 2025 | YOLO11 tumor + tool tracking on ultrasound; 1.2 ms/frame GPU | Real-time evaluation design
Yeung et al., 2024 | 16 models; Dice 0.959 but specificity 0.433 | Why we measure margin in mm
Veluponnar et al., 2023 | Ensemble segmentation, ultrasound; margin ≥ 2 mm | Mask-to-margin conversion
Maris et al., 2025 | ResU-Net on micro-PET-CT, 28 patients | Margin evaluation vs. readers
arXiv:2404.10600, 2024 | Threshold + SegNet on specimen mammograms | Closest to our pipeline
Amgad et al., 2019 | BCSS: 151 H&E slides, 20,000+ regions | Our training data
Alhsnony & Sellami, 2024 | YOLOv8-seg on mammograms | Training setup reference
Zheng et al., 2026 | YOLOv8 vs. YOLOv12 in colon surgery video | YOLO version comparison

## Slide 6
Research Gap
6
Existing work uses ultrasound, PET-CT or mammography, not light-microscope histology
Shao 2025 uses bounding boxes and reports no distance in mm
The closest margin pipeline (arXiv 2024) reports a large error of 6.53 ± 5.84 mm
No study quantifies domain shift from a public dataset to a university microscope with an ablation of each fix
Our contribution: margin distance in mm on microscope images, distance error as the primary metric, and a quantitative domain-shift study

## Slide 7
Input and Output
7
Input
Microscope camera frames (live or recorded) of H&E breast tissue
Calibrated resolution (µm per pixel)
Configurable alert threshold
Output
Tumor segmentation mask overlay
Shortest tumor-to-edge distance in mm
Margin alert when below threshold
Latency per frame (target ≈ 40 ms)
Optional rule-based PDF report

## Slide 8
Data and Database
8
Phase 1: BCSS (public)
151 H&E whole-slide cases, CC0 license
Resampled to 1.0 px/µm, 512×512 patches
Patient-level train/val/test split
Tumor masks converted to YOLO polygons
Phase 2: Local samples
University microscope images, calibrated with a stage micrometer
Healthy animal tissue and lymph node as negative controls
Archived human breast H&E slides from a hospital, after ethics approval
Labeled by a pathologist (Labelme / QuPath)

## Slide 9
Methodology
9
Phase 1
Model & training
BCSS preparation and split
Stain normalization (Macenko)
YOLOv8-seg / YOLO11-seg vs. U-Net or SegFormer
Dice, IoU, bootstrap CIs
Phase 2
Lab adaptation
Microscope calibration
Zero-shot test, then fine-tuning
Margin = distance transform on tumor mask and tissue edge
Real-time OpenCV pipeline
Phase 3
Decision support
Rule-based margin status
Guideline retrieval (ChromaDB)
Automatic PDF report
Final evaluation and paper

## Slide 10
Summary
10
Goal: measure tumor margin in mm from microscope images, in real time
Approach: YOLO-Seg trained on BCSS, adapted to lab images with calibration and stain normalization
Primary metric: distance error in mm, plus Dice/IoU and ms per frame
Contribution: fills the histology-microscope gap and quantifies domain shift
Limits: proof of concept on archived FFPE samples, not a clinical device