## Slide 1: AI-Assisted Tumor Segmentation and Margin Distance Estimation in Breast Histopathology Images
A Proof-of-Concept Study
Prepared by
Hala Hamza Rawashdeh
Razan Mohammad Essam Al-Jabban
Supervised by
Dr. Nisreen Suleiman
Eng. Zainab Baghdadi
Faculty of AI Engineering · Syrian Private University · 2026–2027

## Slide 2: Introduction: Why Margins Matter
≈20%
of invasive-cancer patients have a positive margin after the first excision
Maris et al., 2025
3–5 days
typical wait for the pathology margin result
Maris et al., 2025
2 mm
alert threshold used in this project (configurable)
Close-margin definition: Veluponnar, 2023
margin = ? mm
tumor
tissue edge
H&E tissue section (schematic)
Idea: segment the tumor on microscope images and measure the margin in millimetres, live. A proof of concept for decision support, not a medical device.

## Slide 3: Problem Statement
Clinical need
Margin results arrive days late
Positive margin means a second surgery
Technical challenge
Segment the tumor, then measure in mm
Domain shift: public data vs. our microscope
Evaluation issue
High Dice does not guarantee a correct margin call
We need mm error and latency per frame

## Slide 4: Literature Review: Three Directions
Ultrasound navigation
Shao et al., 2025
Veluponnar et al., 2023
Yeung et al., 2024
Real-time, but boxes or classes
Specimen imaging
Maris et al., 2025
arXiv:2404.10600, 2024
Ward et al., 2025
Mask to margin, large errors
Histology and methods
Amgad et al., 2019 (BCSS)
Multi-magnification net, 2021
Alhsnony & Sellami, 2024
Zheng et al., 2026
Cell-level detail, offline

## Slide 5: Direction 1: Ultrasound Navigation
Shao, 2025
YOLO11 tracks the tumor and the tool in real time
1.2 ms
per frame on GPU
Boxes only, no mm
Veluponnar, 2023
Ensemble of 8 networks on lumpectomy ultrasound
96% / 76%
sensitivity / specificity for close margin (≤ 2 mm)
Median Dice 0.88
Yeung, 2024
16 models, 7,318 images from 33 patients
0.959 vs 0.433
Dice vs. specificity against pathology
Weak margin call
Takeaway: fast and promising, but good segmentation alone does not guarantee a correct margin decision.

## Slide 6: Direction 2: Specimen Imaging
Maris, 2025
ResU-Net on micro-PET-CT images of lumpectomy specimens
28
patients in the segmentation data set
Margin vs. histology
arXiv:2404.10600
Thresholding + SegNet on specimen mammograms
6.53 ± 5.84 mm
mean gap to manual margin, 30 cases
Closest to ours
Ward, 2025
SAM refines coarse masks on specimen radiographs
AUC 0.846
margin classification, 47 ms per image
Image-level output
Context: specimen mammography, widely used intra-operatively, has a pooled sensitivity of only 0.55 (meta-analysis, 20 studies).

## Slide 7: Direction 3: Histology and Methods
Amgad et al., 2019
BCSS: 151 H&E slides, 20,000+ annotated regions
Our training data
Multi-magnification net, 2021
Segments carcinoma on scanned shave-margin slides
Histology margin work, but offline
Alhsnony & Sellami, 2024
YOLOv8-seg for breast lesions on mammograms
Training-setup reference
Zheng et al., 2026
YOLOv8 vs. YOLOv12 on colon-surgery video
YOLO version comparison
The 2021 histology study works on whole-slide scans after the operation, not on live microscope frames.

## Slide 8: What the Literature Tells Us
0.959
Dice, yet only 0.433 specificity
High Dice does not guarantee a correct margin call
6.53 mm
error of a distance-based pipeline
Margins must be judged in millimetres
1.2 ms
per frame for real-time YOLO
YOLO-class models are fast enough for live use
0.55
pooled sensitivity of specimen mammography
Intra-operative tools leave room to improve

## Slide 9: Where Our Work Fits
Direction | What it delivers | What is missing
Ultrasound navigation | Real-time boxes or masks; margin class | No distance in mm; Dice is not margin accuracy
Specimen imaging | Margin status or width from specimen images | Large errors (6.53 mm); no cellular detail
Histology (scanned slides) | Accurate tissue segmentation | Offline; no live microscope; no mm distance
Our proof of concept | YOLO-seg on H&E, distance in mm, live frames | Domain-shift study: public data to our microscope

## Slide 10: Research Gap
1
Real-time margin AI relies on ultrasound, PET-CT or mammography, not on microscope histology
2
Closest works: boxes only (Shao, 2025) or a 6.53 ± 5.84 mm error (arXiv, 2024)
3
No study we found quantifies domain shift from a public dataset to a university microscope, fix by fix
Our contribution: margin distance in mm on microscope images, distance error as the primary metric, and a quantitative domain-shift study

## Slide 11: Input and Output
Input
Microscope frames, live or recorded
Calibration in µm per pixel
Configurable alert threshold
YOLO-seg
+ distance transform
Output
Tumor mask overlay
Shortest tumor-to-edge distance (mm)
Margin alert below threshold
Latency per frame (target ≈ 40 ms)
Optional PDF report

## Slide 12: Data and Database
Phase 1: BCSS (public)
151
H&E whole-slide cases, CC0 license
1.0 µm/px, 512×512 patches
Patient-level train/val/test split
Tumor masks converted to YOLO polygons
Phase 2: Local samples
University microscope images, calibrated with a stage micrometer
Healthy animal tissue and lymph node as negative controls
Archived human breast H&E slides, after ethics approval
Labeled by a pathologist (Labelme / QuPath)

## Slide 13: Methodology
1
Phase 1: Model and training
BCSS preparation and split
Macenko stain normalization
YOLOv8-seg / YOLO11-seg vs. U-Net or SegFormer
Dice, IoU, bootstrap CIs
2
Phase 2: Lab adaptation
Microscope calibration
Zero-shot test, then fine-tuning
Margin = distance transform on mask and tissue edge
Real-time OpenCV pipeline
3
Phase 3: Decision support
Rule-based margin status
Guideline retrieval (ChromaDB)
Automatic PDF report
Final evaluation and paper

## Slide 14: Summary
Goal
Measure tumor margin in mm from microscope images, in real time
Approach
YOLO-seg trained on BCSS, adapted with calibration and stain normalization
Metric
Distance error in mm, plus Dice/IoU and ms per frame
Contribution
Fills the histology-microscope gap and quantifies domain shift
Limits
Proof of concept on archived FFPE samples, not a clinical device

## Slide 15
Thank you